ATI sonic configuration
serial port: 9600 E 7 1
Data quality algorithm (ON)
Shadow correction (ON)
Remove RH from temp calc (OFF or ON/RH=0)
U,V,W,Ts @ 10hz output
Data pipeline lag: 1/10th sec
ATI_recorder_v1.cr1
User-Editable Constants
Description	Name	Value
Number of days of data retention	DAYS_OF_DATA_STORAGE	14
Azimuth of sonic on COM1	AZIMUTH_1	0
Azimuth of sonic on COM2	AZIMUTH_2	0
Azimuth of sonic on COM3	AZIMUTH_3	0
Azimuth of sonic on COM4	AZIMUTH_4	0
Local magnetic declination, added to azimuths; use 0 if azimuths are relative to true north	DECLINATION	0

PS100 Battery Charger / Power Regulator
POWER IN
one	18vDC laptop power supply (+)
other	18vDC laptop power supply (-)
POWER OUT
12V	CR3000 power in (+) / network switch (+)
G	CR3000 power in (-) / network switch (-)
BATTERY CONN
(+)	deep cycle batt (+)
(-)	deep cycle batt (-)

CR3000 Data Logger
POWER IN		POWER OUT
12V	PS100 regulator (+)	12V	ATI sonics' power (+)
G	PS100 regulator (-)	G	ATI sonics' power (-)
		SWITCHED POWER OUT
		SW-12V	enclosure fan (+)
		G	enclosure fan (-)
COM PORTS via four-way DB9 adapter
COM1		ATI sonic 1 data
COM2		ATI sonic 2 data
COM3		ATI sonic 3 data
COM4		ATI sonic 4 data